REQUEST FOR QUOTATION (RFQ)

for the

# Construction of the IOM Office – 25th Floor Tower 6789 (Ayala Avenue)

# BID BULLETIN

# Addendum No. 1

This Addendum No. 01 is issued to modify information provided in the Request for Quotation and General Instructions to Suppliers for the Construction of the IOM Office – 25th Floor Tower 6789 issued to the prospective Suppliers on July 14, 2017.

A. Inquiries from vendors

1.	Q.	The architect reiterated that the layout/ drawings only reflect the architectural perspective, will IOM provide the As-built (electrical, mechanical, etc.)?

A. 	The Tower 6789 Building Admin through IOM will provide the requested plans for reference purposes.

2.	Q.	What is the specification of the electrical?

- Tower 6789: “The electrical supply voltage is 400V/3Phase/60 Hz.”

Assumed Internal Heat Load sources:

o 1.0 People = 230 Btu/Hr. Sensible Heat & 120 Btu/Hr. Latent Heat

o 2.0 Lights = 21.53 Watts/m² x 1.25 Ballast Multiplier

o 3.0 Equipment Heat Emission = 32 Watts/m²

IOM explained that building requirements are indicated in the Tower 6789 Construction Guidelines which will be shared via email to all the participating contractors.

IOM Architect further explained the layout/ drawings:

- Contractors to refer to IOM-6789-CD-04 on the areas where the flooring is to be raised.

- For the structure cabling under Scope of Work (SW) B.7 – Telecommunications, quote should include provision of 1 data and 1 voice port.

- Tower 6789 has accredited contractors for Fire Detection (sprinkler, smoke detector, etc): PULSER ENTERPRISES; Hotworks: PHILIPPINE PLUMBING CONTRACTOR INC.

- Bill of Quantities (BOQ) in excel format will be forwarded via email or posted in the IOM website. Contractors must fill-out the cells in light blue. Note that the contents in other cells are protected and therefore not editable. Should there be additional items or observations contractors may use the unlocked cells out of the print section.

| Jack Ocureza Fire Protection 0919-5391270 | Mafe Nacional PULSER Fire Detection Alarm System 0922-8225745 |
| --- | --- |

Last day of submission of questions and clarifications (by email only) on is extended until 12PM of July 24, 2017 (Monday).

Reminder: All bidding documents are to be submitted at the IOM Office, 28th Floor Citibank Tower, 8741 Paseo de Roxas, Makati City.