ANNEX A - CHECKLIST FOR TECHNICAL PROPOSAL

| No. | Document |
| --- | --- |
|  |  | Submitted |
| 1 | Vendor’s Expertise and Qualifications |  |
| 2 | Vendor’s understanding on the required methodology |  |
| 3 | Schedule of Technical data |  |
| 4 | Schedule of Required Certifications |  |
| 5 | Quality Management System |  |
| 6 | Warranty/Guarantee |  |

TECHNICAL SPECIFICATIONS			Annex B

| Ref No. : ____________________ Item No. : ____________________ Item Description : ____________________ |
| --- |
| Manufacturer : ________________________________________________ Origin : ________________________________________________ Model : ________________________________________________ |
| IOM’S SPECIFICATIONS | BIDDER'S SPECIFICATIONS And indicate COMPLY or NOT COMPLY |
| Brand New (2017 model) 4x4, Middle-East or Tropical Version LHD Toyota GXR LC200, V8 petrol engine 4.6L, with high altitude compensator, automatic transmission, white colored, and fully certified armoring level: Option 1: VR6 Option 2: VR7 Please offer 2 options. |  |
| Inclusion: MOSS Accessories: (to be installed at the armoring factory) 1. Heavy Duty Bull Bar 2. Warn Electric Winch – 12 V – 6 tons capacity 3. Driver Side Window Lifter 4. Heavy Duty Jack (5,000kgs) 5. Bulb Fuse Kit 6. Fire extinguisher 2Kg 7. 2nd Spare Wheel Incl. Runflat 245/75R17 11. Wheel Wrench X-Type, 17,19,21 (13/16) 22mm 12. Tow Rope (5,000kgs) 5 meters 13. Jumper cables SUPER HEAVY DUTY 500 amp 6 gauge 12 feet with travel case 14. Winch Recovery Accessories In Storage Bag 15. Rear cargo area anchor points & elasticated net 16. First aid kit 17. Rechargeable torch light 18. Warning triangle 19. GPS tracking system to track the movement of the AV operating under the local GSM network grid and not via Satellite. 20 Motorola GM360 (VHF) 255 Channel, 25W & Remote Mount Kit 21.Thuraya Vehicle Docking Adaptor (Handset not included)- Southern Hemisphere & External Mag Antenna 22. Codan HF Mobile Radio, NGT SRx with 9350 Antenna, 400 Channels 23. Replacement Rear Bumper Bar, Including Hi-Lift Jacking Points 24. Four cameras with resolution 1080 HD, with recording capacity up to 48 hrs (not less): One mounted in front with wide view of the front road; One mounted in the back with wide view of the rear; One with wide view, mounted in the front upper corner, above the windshield, in front of passenger seat with view of the passenger, driver and back seats; One mounted with view on the outside the driver’s window, i.e. to record anyone approaching the driver. 25. A siren, intercom and public address system, of European manufacture, must be installed with switching and handset located in the front compartment in such a way as to enable equal ease of operation by both the driver and the front passenger who is usually a security officer and will usually operate this equipment. The siren should only provide one distinct acoustic sound; the variable type is not required. Equipment may not be installed in the glove box. NOTE: All communication equipment must be air lifted and only required wiring should be installed in the car. |  |
| Additional Accessories: Engine Bay Armour Pre-wiring for VHF radio installation Secondary rear view mirror Garage Jack,4T capacity Nylon Snatchstrap, ARB 9Meters.3T U-Bolts, x2, D shackles, 6 5T 2 Years spare parts pack, Extra spare key |  |
| Other Requirement: 1. The back compartment: the back armored wall shall be installed at the very end of the vehicle allowing to include 2 additional protected back seats behind the main back seat. 2. Smooth and professional finishing. 3. No rough edged shall be left not properly finishing especially for the steel works. 4. No rough edged shall be left not properly finishing especially for the steel works. 5. Steel frame on the front windshield should be protected by a rubber covers to avoid being rust also to avoid injuring hands. 6. Steel frame on the front windshield should be protected by a rubber covers to avoid being rust also to avoid injuring hands. 7. The towing hook at the rear bumper shall be from the closed type (not the open type). 8. A rear power source shall be installed to light up the towed compartment. 9. A full welded metal front bull bar (not nickel and/or any fragile material) shall be also extended to cover the front lights as well (not only the middle part of the engine). 10. The back armored door (bulk head door) shall have a latch from inside to prevent access to the AV from outside. 11. The engine compartment shall be properly sealed with some metal or Kevlar material through the hood (hood protection). The hood has a proper locking system that will prevent it from flying out to block driver view. 12. Engine bay fire system should be installed. |  |
| Additional Spare Parts Request: # Spare Parts Package Unit of Measure Qty 1 Front Rotor Pair 2 2 Rear Rotor Pair 2 3 Front Brake Pads Pair 10 4 Rear Brake Pads Pair 8 5 Air Filter K&N Reusable EA 2 6 Fuel Filter EA 3 7 In Cabin Air Filter EA 2 |  |
| Exclusion: video screens behind the middle seats |  |

Notes and Reminders:

Radio Equipment:

Radios and communications systems must be installed during the armoring process. Each RFQ must specify the types of radios required. The radio and sat phone communications equipment must be positioned in the front compartment in such a way as to enable equal ease of operation by both the driver and the front passenger (the space between the driver and passenger seat may be utilized but changing of channels and operation of equipment must be possible without stopping the vehicle). All wiring must be run through pre-installed conduit tubing so as to facilitate the ease of any post-manufacture replacement and/or maintenance of wiring and equipment. Wiring must be incorporated in the certified armoring design and manufacture in order to prevent the creation of gaps in the armor during the installation of the equipment. Manuals must be provided for the radios and sat phone communications equipment. Equipment should not be installed in the glove box. Items are:

- Full Package Motorola VHF Radio Mobile Station GM360 with all accessories and antenna, 255 Channel, 25W & Remote Mount Kit. The VHF antennae must be securely fitted to one of the front fenders of the vehicle, and not the roof. Magnetic mounting will not be accepted.

- Full Package Codan HF Radio Mobile Station, NGT SRx with 9350 Antenna, 400 Channels with all accessories (GPS enabled). The HF antennae should preferably be installed at the rear of the vehicle.

- Full Package Iridium Sat Phone Car Docking Station (handset not included) for handset Model 9555, or, Thuraya Vehicle Docking Station (Handset not included)– Southern Hemisphere & External Mag Antenna, including charging-cradle, headset and external antennae, to be installed during the armoring process.

IMPORTANT:

You need to install only the wiring of all the communications at your armoring factory. Any other visible components like; handsets, loudspeakers, GM380 main unit, external antennas and brackets, GPS tracer, SAT phone docking station, etc.. all should NOT be installed but to be packed and airlifted by courier service to Sana’a Airport separately (in one single shipment) as it has another customs clearance lengthy process.

| ITEM NO. | ITEM DESCRIPTION | COUNTRY OF ORIGIN | QUANTITY | UNIT | UNIT PRICE | TOTAL PRICE | DELIVERY SCHEDULE including period of vehicle acquisition, armoring, installation of accessories, processing of export licenses and sea transit | DELIVERY SITE /FINAL DESTINATION |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Offered Vehicle per Annex B |  |  |  |  |  |  |  |
| 2 | Spare Parts List and Price (indicate discount rate if any) |  |  |  |  |  |  |  |
| TOTAL |  |  |  |  |  |  |  |  |

Annex C

PRICE SCHEDULE FORM

PROJECT TITLE	  :     Supply and Delivery of Armored Vehicles for IOM Sanaa Yemen

REF NO.                 :     RFQ2017.025. YEMEN

________________________________________

Suppliers authorized signature over printed name

Annex D

VENDORS INFORMATION SHEET (VIS)

Name of the Company   __________________________________________________________

Address		Leased			Owned		Area: _______sqm

House No        _____________________________________________________

Street Name    _____________________________________________________

Postal Code     _____________________________________________________

City                  _____________________________________________________

Region             _____________________________________________________

Country            _____________________________________________________

Contact Numbers/Address

Telephone Nos. __________________   Contact Person:  ___________________

Fax No.		____________________

E mail Address	____________________ Website:  ___________________

Location of Plant/Warehouse		Leased		Owned		Area: ______sqm

__________________________________________________________________

__________________________________________________________________

__________________________________________________________________

Business Organization	Corporation	     Partnership		Sole Proprietorship

Business License No.: __________ Place/Date Issued:_________ Expiry Date ________

No. of Personnel ___________ Regular ___________ Contractual/Casual ____________

Nature of Business/Trade

Manufacturer			Authorized Dealer		Information Services

Wholesaler			Retailer			Computer Hardware

Trader				Importer			Service Bureau

Site Development/		Consultancy			Others ____________

Construction							__________________

Number of Years in business:  _________

Complete Products & Services

__________________________________________________________________

__________________________________________________________________

Payment Details

Payment Method	Cash		Check		Bank Transfer		Others

Currency		Loc.Currency		USD		EUR		Others

Terms of Payment	 30 days		15 days		7 days	upon receipt of invoice

Advance Payment	Yes			No		% of the Total PO/Contract

Bank Details:

Bank Name		________________________________________________

Bldg and Street	________________________________________________

City			________________________________________________

Country		________________________________________________

Postal Code		________________________________________________

Country		________________________________________________

Bank Account Name	________________________________________________

Bank Account No.	________________________________________________

Swift Code		________________________________________________

Iban Number 		________________________________________________

Key Personnel & Contacts (Authorized to sign and accept PO/Contracts & other commercial documents)

Name				Title/Position			Signature

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

Companies with whom you have been dealing for the past two years with approximate value in US Dollars:

Company Name		Business Value		Contact Person/Tel. No.

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

Have you ever provided products and/or services to any mission/office of IOM?

Yes			No

If yes, list the department and name of the personnel to whom you provided such goods and/or services.

Name of Person		Mission/Office			Items Purchased

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

Do you have any relative who worked with us at one time or another, or are presently employed with IOM?  If yes, kindly state name and relationship.

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

Trade Reference

Company			Contact Person			Contact Number

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

Banking Reference

Bank				Contact Person			Contact Number

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

_______________________	_______________________	_______________________

REQUIREMENTS CHECK LIST

Please submit the following documents together with the Information Sheet:

| No. | Document | For IOM use only |
| --- | --- | --- |
|  |  | Submitted | Not Applicable |
| 1 | Company Profile (including the names of owners, key officers, technical personnel) |  |  |
| 2 | Company's Articles of Incorporation, Partnership or Corporation, whichever is applicable, including amendments thereto, if any. |  |  |
| 3 | Certificate of Registration from host country's Security & Exchange Commission or similar government agency/department/ministry |  |  |
| 4 | Valid Government Permits/Licenses |  |  |
| 5 | Audited Financial Statements for the last 3 years* |  |  |
| 6 | Certificates from the Principals (e.g. Manufacturer's Authorization, Certificate of Exclusive Distributorship, Any certificate for the purpose, indicating name, complete address and contact details) |  |  |
| 7 | Catalogues/Brochures |  |  |
| 8 | List of Plants/Warehouse/Service Facilities |  |  |
| 9 | List of Offices/Distribution Centers/Service Centers |  |  |
| 10 | Quality and Safety Standard Document / ISO 9001 |  |  |
| 11 | List of all contracts entered into for the last 3 years (indicate whether completed or ongoing ) * |  |  |
| 12 | Certification that Non-performance of contract did not occur within the last 3 years prior to application for evaluation based on all information on fully settled disputes or litigation |  |  |
| 13 | For Construction Projects: List of machines & equipment (include brand, capacity and indication if the equipment are owned or leased by the Contractor) |  |  |

* For Competitive Biddings, number of years may increase depending on the estimated contract amount.

** Indicate if an item is not applicable. Failure to provide any of the documents mentioned above will result in automatic "failed" rating.

I hereby certify that the information above are true and correct. I am also authorizing IOM to validate all claims with concerned authorities.

Received by:

_______________________				_______________________

Signature						Signature

_______________________				_______________________

Printed Name 					   Printed Name

_______________________				______________________

Position/Title						 Position/Title

_______________________				_______________________

Date							Date

__________________________FOR IOM USE ONLY_________________________

Purchasing Organization	___________________

Account Group		___________________

Industry 		001			002			003

where 	001  - Transportation related to movement of migrants

002 - Goods (e.g. supplies, materials, tools)

003 - Services (e.g. professional services, consultancy, maintenance)

Vendor Type		Global			Local

# Text boxes

FPU.SF-19.2